Klar: Midi Mapping and implementation (Midi Channel 5):
Command	byte 1	byte 2	default	range	remarks & function
Note Off	note	release	-	43-106	release, if not zero, sets controller 19 to the value 128 - release.
Note On	note	velocity	-	43-106	optimum: 43-91
Controller	1	value	1	0-127	Wind controller, steers the amount of noise in the sound
	2	value	2	0-127	LFO3 frequency applied to the filter.
	3	value	20	0-127	Vibrato depth (LFO1 amplitude).
	4	value	8	0-127	Vibrato speed. (LFO1 frequency).
	5	value	0	0-127	Tremolo depth, amplitude modulation. (LFO2).
	6	value	0		Tremolo speed. (LFO2 frequency).
	7	value	80		Global volume control. Can be used for crescendo and decrescendo effects whilst notes are sounding. This also affects the sound color of the instrument, as normal for clarinets.
	16	value	100		Note attack speed controller (0= slow attack, 127= fast attack) .
	17	value	127		Attack level: used to control the maximum sound level reached after the attack time. This controller is always larger than or equal to the level set by the velocity byte. For sfz or staccato playing, this controller must be set to high levels and the velocity byte kept rather low
	18	value	90		is used to control the speed of the transition between the attack level once reached and the sustain or hold value set by the velocity byte.(0= slow transition, 127= fast transition)
	19	value	96		used to control the release time after reception of a note off. Here again a value of 0 will give a slow release whereas a value of 127 will give a very fast release. Note that with very low values, the note may not even turn off completely. Note that if real note-off commands are used, the release value sent with them, if this value is not zero, will override controller 19, such that the value of controller 19 will be set to 128-release value.
	20	value	64	0-127	Basic tuning of the instrument , range -/+ a semitone. 64 = 440Hz
	22	value	64	32-96	Vertical inclination controller. (0-63= backwards, 64=central, unpowered, 65-127= forwards). At extreme positions the holding power of the motor will not be high enough to hold the clarinet in place and as a result, the instrument will oscillate.
	24	value	0		0 = motor in half step mode, any other value: motor in full step mode (for development only).
	25	value	62		Filter cut off frequency. Determines the placement of the formant in the spectrum and thus influences the color of the instrument.
	26	value	90		Filter resonance amount. Q-factor for the filter frequency set with controller 25
	27	value	0		Echo mix. Only use this for experimental sounds, as it can generate multiphonics.
	28	value	0		echo feedback.Only use this for experimental sounds, as it can generate multiphonics.
	29	value	20		LFO3, filter depth. (large values give a wha-wha effect)
	30	value	100		Valve release time out.(only used for code development)
	31	value	0		Does the same thing as aftertouch: fingered vibrato. However, it does not require to be sent again and again in a sequencer. The parameter sets the fingered vibrato speed. Default = 0
	40		1		Bendrange for the pitchbend. 0= no bending, 1=+/- 50 cents.
	41		62		Duodecime component detune. Herewith we can detune the duodecime partial just a bit. This causes slow beats in the sound. With setting = 64, there are no beats.
	42		120		Duedecime component amplitude
	43		100		Wait time for vibrato start after reception of a note-on command. Note that in legato playing, vibrato will continue. The wait time starts again after a note off is received.
	44		10		Wait time for the tremolo (AM modulation) to start after a note-on command.
	66		0		Power on/off switch (0 = off, any other value is on). Power off, resets all controllers to their cold-boot values.
	100		0		special fingerings , bit settings for valves 1 to 7
	101		0		special fingerings, bit settings for valves 8 to 14
	102		0		special fingerings, bit settings for valves 15 to 21
	123		x		switches the sounding note off, unpowers the stepper motor, dims all the lights. Does not reset any controllers.
Channel aftertouch		value	0		used for implementing fingered vibrato. The parameter sets the vibrato speed. Note that timbral vibrato cannot be consistently applied to all notes! For note 43 for instance, all valves are closed and there is simply no valve to use for vibrato. In this case we activate the overblow valve as vibrato valve. Sending the fingered vibrato command is harmless at any time. If it is impossible, nothing will happen. The parameter sets the speed wherewith the vibrato is performed. Note that most sequencers reset the channel aftertouch after every note off. To overcome that problem, we have implemented controller 31 as an alternative.
Program change		value	0		not implemented so far. Will be used later for interactive robotic modes of functioning, exploiting the audio input possibilities on the ARM-board.
Pitchbend	lsb	msb			with bendrange set to 1, each increment/decrement corresponds to a cent.

Lights: The lights are mapped on very high midi-notes as follows:
- note 126: frontal red LED strip light (on/off) [F#10]
- note 125: blue LED strip light on the backside, left (on/off) [F10]
- note 124: blue LED strip light on the backside, right (on/off) [E10]
- note 123: tungsten white (halogen) upwards under the front of the instrument., This light is dimmable. The velo byte steers the brightness. Flashing is implemented but required the use of the note-pressure command after the note on. [Eb10]
- note 122: white LED strip in the front, dimmable. The velo byte steers the brightness. Flashing is implemented but required the use of the note-pressure command after the note on. [D10]
- note 121:frontal blue (the velo byte steers the flashing speed, with 127 it is always ON) [C#10]
- note 120: frontal blue (the velo byte steers the flashing speed, with 127 it is always ON) [C10]
Classified by function, we have the following groups of controllers:
- Note Off, with release byte implemented
- Note On: ADSR: CC16,17,18,19, velocity byte
- Tuning related controllers: CC20, pitchbend, CC40, CC41
- Vibrato: CC3, CC4, CC31, CC43
- Tremolo: CC5, CC6, CC44 (can also be used to implement Flatterzunge effects)
- Sound color: CC2, CC25, CC26, CC29, CC42
- Effects: CC22, CC23