Fa: Midi Mapping and implementation (Midi Channel 15):
Command	byte 1	byte 2	default	range	remarks & function
Note Off	note	release	-	34-91	release, if not zero, sets controller 19 to the value 128 - release.
Note On	note	velocity	-	34-91	optimum: 34-79
Controller	1	value	1	0-127	Wind controller, steers the amount of noise in the sound
	2	value	3	0-127	LFO3 frequency applied to the filter.
	3	value	20	0-127	Vibrato depth (LFO1 amplitude).
	4	value	14	0-127	Vibrato speed. (LFO1 frequency).
	5	value	0	0-127	Tremolo depth, amplitude modulation. (LFO2).
	6	value	0		Tremolo speed. (LFO2 frequency).
	7	value	64		Global volume control. Can be used for crescendo and decrescendo effects whilst notes are sounding. This also affects the sound color of the instrument, as normal for clarinets.
	16	value	80		Note attack speed controller (0= slow attack, 127= fast attack) .
	17	value	127		Attack level: used to control the maximum sound level reached after the attack time. This controller is always larger than or equal to the level set by the velocity byte. For sfz or staccato playing, this controller must be set to high levels and the velocity byte kept rather low
	18	value	90		is used to control the speed of the transition between the attack level once reached and the sustain or hold value set by the velocity byte.(0= slow transition, 127= fast transition)
	19	value	72		used to control the release time after reception of a note off. Here again a value of 0 will give a slow release whereas a value of 127 will give a very fast release. Note that with very low values, the note may not even turn off completely. Note that if real note-off commands are used, the release value sent with them, if this value is not zero, will override controller 19, such that the value of controller 19 will be set to 128-release value.
	20	value	64	0-127	Basic tuning of the instrument , range -/+ a semitone. 64 = 440Hz
	21	value			motor
	22	value	64		Vertical inclination controller.
	23	value			motor
	24				Reserved (used in Klar) / Not implemented on <Fa>
	25	value	75		Filter cut off frequency. Determines the placement of the formant in the spectrum and thus influences the color of the instrument. Never use values lower than 66.
	26	value	100		Filter resonance amount. Q-factor for the filter frequency set with controller 25
	27	value	0		Echo mix. Only use this for experimental sounds, as it can generate multiphonics.
	28	value	0		echo feedback.Only use this for experimental sounds, as it can generate multiphonics.
	29	value	21		LFO3, filter depth. (large values give a wha-wha effect)
	30	value	100		Valve release time out.(only used for code development)
	31	value	0		Does the same thing as aftertouch: fingered vibrato. However, it does not require to be sent again and again in a sequencer. The parameter sets the fingered vibrato speed. Default = 0
	40		1		Bendrange for the pitchbend. 0= no bending, 1=+/- 50 cents.
	41		64		Duodecime component detune. Herewith we can detune the duodecime partial just a bit. This causes slow beats in the sound. With setting = 64, there are no beats. / Do not use this on <Fa>
	42		0		Duedecime component amplitude / Do not use this on <Fa>
	43		20		Wait time for vibrato start after reception of a note-on command. Note that in legato playing, vibrato will continue. The wait time starts again after a note off is received.
	44		10		Wait time for the tremolo (AM modulation) to start after a note-on command.
	50				Formant frequency (500Hz) Not yet implemented
	51				Resonance amount for the formant. Not yet implemented.
	66		0		Power on/off switch (0 = off, any other value is on). Power off, resets all controllers to their cold-boot values.
	100		0		special fingerings , bit settings for valves 1 to 7
	101		0		special fingerings, bit settings for valves 8 to 14
	102		0		special fingerings, bit settings for valves 15 to 21
	103		0		special fingerings, bit settings for valves 22 to 29
	123		x		switches the sounding note off, unpowers the motor, dims all the lights. Does not reset any controllers.
Channel aftertouch		value	0		used for implementing fingered vibrato. The parameter sets the vibrato speed. Note that timbral vibrato cannot be consistently applied to all notes! For note 43 for instance, all valves are closed and there is simply no valve to use for vibrato. In this case we activate the overblow valve as vibrato valve. Sending the fingered vibrato command is harmless at any time. If it is impossible, nothing will happen. The parameter sets the speed wherewith the vibrato is performed. Note that most sequencers reset the channel aftertouch after every note off. To overcome that problem, we have implemented controller 31 as an alternative.
Program change		value	0		not implemented so far. Will be used later for interactive robotic modes of functioning, exploiting the audio input possibilities on the ARM-board.
Pitchbend	lsb	msb			with bendrange set to 1, each increment/decrement corresponds to a cent.

Lights: The lights are mapped on very low midi-notes as follows:
Classified by function, we have the following groups of controllers:
- Note Off, with release byte implemented
- Note On: ADSR: CC16,17,18,19, velocity byte
- Tuning related controllers: CC20, pitchbend, CC40
- Vibrato: CC3, CC4, CC31, CC43
- Tremolo: CC5, CC6, CC44 (can also be used to implement Flatterzunge effects)
- Sound color: CC2, CC25, CC26, CC29
- Effects: CC22, CC23